## Slide 1: CS3014: Computer Architecture
Superscalar Pipelines
Slides developed by Joe Devietti, Milo Martin & Amir Roth at U. Penn with sources that included University of Wisconsin slides by Mark Hill, Guri Sohi, Jim Smith, and David Wood

## Slide 2: This Unit: (In-Order) Superscalar Pipelines
Idea of instruction-level parallelism
Superscalar hardware issues
  Bypassing and register file
  Stall logic
  Fetch
CPU
Mem
I/O
System software
App
App
App

## Slide 3: “Scalar” Pipeline
So far we have looked at scalar pipelines
  One instruction per stage
    With control speculation, bypassing, etc.
  Performance limit is CPI = IPC = 1
    CPI – cycles per instruction
    IPC – instructions per cycle
  Limit is never even achieved (hazards)
  Diminishing returns from deeper pipelines (hazards + overhead)
regfile
D$
I$
B
P

## Slide 4: An Opportunity…
But consider:
  ADD r1, r2 -> r3
  ADD r4, r5 -> r6
  Why not execute them at the same time? (We can!)
What about:
  ADD r1, r2 -> r3
  ADD r4, r3 -> r6
  In this case, dependences prevent parallel execution
What about three instructions at a time?
  Or four instructions at a time?

## Slide 5: What Checking Is Required?
For two instructions: 2 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
For three instructions: 6 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
For four instructions: 12 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
  ADD src14, src24 -> dest4 (6 checks)
Plus checking for load-to-use stalls from prior n loads

## Slide 6: What Checking Is Required?
For two instructions: 2 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
For three instructions: 6 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
For four instructions: 12 checks
  ADD src11, src21 -> dest1
  ADD src12, src22 -> dest2 (2 checks)
  ADD src13, src23 -> dest3 (4 checks)
  ADD src14, src24 -> dest4 (6 checks)
Plus checking for load-to-use stalls from prior n loads
Notes: What are checks? Why not check all-to-all?

## Slide 7: How do we build such “superscalar” hardware?

## Slide 8: Multiple-Issue or “Superscalar” Pipeline
Overcome this limit using multiple issue
  Also called superscalar
  Two instructions per stage at once, or three, or four, or eight…
  “Instruction-Level Parallelism (ILP)” [Fisher, IEEE TC’81]
Today, typically “4-wide” (Intel Core i7, AMD Opteron)
  Some more (Power5 is 5-issue; Itanium is 6-issue)
  Some less (dual-issue is common for simple cores)
regfile
D$
I$
B
P

## Slide 9: A Typical Dual-Issue Pipeline (1 of 2)
Fetch an entire 16B or 32B cache block
  4 to 8 instructions (assuming 4-byte average instruction length)
  Predict a single branch per cycle
Parallel decode
  Need to check for conflicting instructions
    Is output register of I1 is an input register to I2?
  Other stalls, too (for example, load-use delay)
regfile
D$
I$
B
P

## Slide 10: A Typical Dual-Issue Pipeline (2 of 2)
Multi-ported register file
  Larger area, latency, power, cost, complexity
Multiple execution units
  Simple adders are easy, but bypass paths are expensive
Memory unit
  Single load per cycle (stall at decode) probably okay for dual issue
  Alternative: add a read port to data cache
    Larger area, latency, power, cost, complexity
regfile
D$
I$
B
P
Notes: why is single load/store per cycle ok?

## Slide 11: Superscalar Implementation Challenges

## Slide 12: Superscalar Challenges - Front End
Superscalar instruction fetch
  Modest: fetch multiple instructions per cycle
  Aggressive: buffer instructions and/or predict multiple branches
Superscalar instruction decode
  Replicate decoders
Superscalar instruction issue
  Determine when instructions can proceed in parallel
  More complex stall logic - O(N2) for N-wide machine
  Not all combinations of types of instructions possible
Superscalar register read
  Port for each register read (4-wide superscalar  8 read “ports”)
  Each port needs its own set of address and data wires
    Latency & area  #ports2

## Slide 13: Superscalar Challenges - Back End
Superscalar instruction execution
  Replicate arithmetic units (but not all, say, integer divider)
  Perhaps multiple cache ports (slower access, higher energy)
    Only for 4-wide or larger (why? only ~25% are load/store insn)
Superscalar register bypass paths
  More possible sources for data values
  O(N2) for N-wide machine
Superscalar instruction register writeback
  One write port per instruction that writes a register
  Example, 4-wide superscalar  4 write ports
Fundamental challenge:
  Amount of ILP (instruction-level parallelism) in the program

## Slide 14: Superscalar Register Bypass
Flow of data between instructions
  Consider the code
  r1 = r3 * r4;
  r7 = r1 + r2;
  The second instruction consumes a value computed by the first
Simple solution
    First instruction writes its result to r1
    Second instruction reads value from r1
    But the write and read take time
    The write-back pipeline stage normally happens at least one cycle later than the execute
    Register read normally happens at least one cycle earlier than execute
    Potential for delay of one or more cycles

## Slide 15: Superscalar Register Bypass
Flow of data between instructions
  Consider the code
  r1 = r3 * r4;
  r7 = r1 + r2;
  The second instruction consumes a value computed by the first
Register Bypassing
  Hardware mechanism to allow data to flow directly from the output of one instruction to the input of another
  The result of the first instruction is written to register r1
  But at the same time a second copy of the result is piped directly to the arithmetic unit that consumes the value
  Requires a hardware interconnection network between the outputs of functional units (such as adders, multipliers) and the inputs of other functional units

## Slide 16: Not All N2 Created Equal
N2 bypass vs. N2 stall logic & dependence cross-check
  Which is the bigger problem?
N2 bypass … by far
  64- bit quantities (vs. 5-bit register indices)
  Multiple levels (MX, WX) of bypass (vs. 1 level of stall logic)
  Must fit in one clock period with ALU (vs. not)
Dependence cross-check not even 2nd biggest N2 problem
  Register file is also an N2 problem (think latency where N is #ports)
  And also more serious than cross-check
Notes: How can we tackle N^2?

## Slide 17: Superscalar Register Bypass
N2 bypass network
  (N+1)-input muxes at each ALU input
  N2 point-to-point connections
  Routing lengthens wires
  Heavy capacitive load
  And this is just one bypass stage!
    Even more for deeper pipelines
  One of the big problems of superscalar
    Why? On the critical path of single-cycle “bypass & execute” loop
versus

## Slide 18: Mitigating N2 Bypass & Register File
Clustering: mitigates N2 bypass
  Group ALUs into K clusters
  Full bypassing within a cluster
  Limited bypassing between clusters
    With 1 or 2 cycle delay
    Can hurt IPC, but faster clock
  (N/K) + 1 inputs at each mux
  (N/K)2 bypass paths in each cluster
Steering: key to performance
  Steer dependent insns to same cluster
Cluster register file, too
  Replicate a register file per cluster
  All register writes update all replicas
  Fewer read ports; only for cluster

## Slide 19: Mitigating N2 RegFile: Clustering++
Clustering: split N-wide execution pipeline into K clusters
  With centralized register file, 2N read ports and N write ports
Clustered register file: extend clustering to register file
  Replicate the register file (one replica per cluster)
  Register file supplies register operands to just its cluster
  All register writes go to all register files (keep them in sync)
  Advantage: fewer read ports per register!
    K register files, each with 2N/K read ports and N write ports
DM
RF0
RF1
cluster 0
cluster 1

## Slide 20: Another Challenge: Superscalar Fetch
What is involved in fetching multiple instructions per cycle?
In same cache block?  no problem
  64-byte cache block is 16 instructions (~4 bytes per instruction)
  Favors larger block size (independent of hit rate)
What if next instruction is last instruction in a block?
  Fetch only one instruction that cycle
  Or, some processors may allow fetching from 2 consecutive blocks
What about taken branches?
  How many instructions can be fetched on average?
  Average number of instructions per taken branch?
    Assume: 20% branches, 50% taken  ~10 instructions
Consider a 5-instruction loop with a 4-issue processor
  Without smarter fetch, ILP is limited to 2.5 (not 4, which is bad)

## Slide 21: Increasing Superscalar Fetch Rate
Option #1: over-fetch and buffer
  Add a queue between fetch and decode (18 entries in Intel Core2)
  Compensates for cycles that fetch less than maximum instructions
  “decouples” the “front end” (fetch) from the “back end” (execute)
Option #2: “loop stream detector” (Core 2, Core i7)
  Put entire loop body into a small cache
    Core2: 18 macro-ops, up to four taken branches
    Core i7: 28 micro-ops (avoids re-decoding macro-ops!)
  Any branch mis-prediction requires normal re-fetch
Other options: next-next-block prediction, “trace cache”
regfile
D$
I$
B
P
insn queue
also loop stream detector
Notes: We saw LSD in the “Getting Wrong Results” paper

## Slide 22: Multiple-Issue Implementations
Statically-scheduled (in-order) superscalar
  What we’ve talked about thus far
  Executes unmodified sequential programs
  Hardware must figure out what can be done in parallel
  E.g., Pentium (2-wide), UltraSPARC (4-wide), Alpha 21164 (4-wide)
Very Long Instruction Word (VLIW)
  Compiler identifies independent instructions, new ISA
  Hardware can be simple and perhaps lower power
  E.g., TransMeta Crusoe (4-wide)
Dynamically-scheduled superscalar (next topic)
  Hardware extracts more ILP by on-the-fly reordering
  Core 2, Core i7 (4-wide), Alpha 21264 (4-wide)

## Slide 23: Trends in Single-Processor Multiple Issue
Issue width has saturated at 4-6 for high-performance cores
  Canceled Alpha 21464 was 8-way issue
  Not enough ILP to justify going to wider issue
  Hardware or compiler scheduling needed to exploit 4-6 effectively
    More on this in the next unit
For high-performance per watt cores (say, smart phones)
  Typically 2-wide superscalar (but increasing each generation)
 | 486 | Pentium | PentiumII | Pentium4 | Itanium | ItaniumII | Core2
Year | 1989 | 1993 | 1998 | 2001 | 2002 | 2004 | 2006
Width | 1 | 2 | 3 | 3 | 3 | 6 | 4