## Slide 1: CS3014: Concurrent Systems
Static & Dynamic Instruction Scheduling
Slides originally developed by Drew Hilton, Amir Roth, Milo Martin and Joe Devietti at University of Pennsylvania

## Slide 2: Instruction Scheduling & Limitations

## Slide 3: Instruction Scheduling
Scheduling: act of finding independent instructions
  “Static” done at compile time by the compiler (software)
  “Dynamic” done at runtime by the processor (hardware)
Why schedule code?
  Scalar pipelines: fill in load-to-use delay slots to improve CPI
  Superscalar: place independent instructions together
    As above, load-to-use delay slots
    Allow multiple-issue decode logic to let them execute at the same time

## Slide 4: Dynamic (Execution-time) Instruction Scheduling

## Slide 5: Can Hardware Overcome These Limits?
Dynamically-scheduled processors
  Also called “out-of-order” processors
  Hardware re-schedules instructions…
  …within a sliding window of instructions
  As with pipelining and superscalar, ISA unchanged
    Same hardware/software interface, appearance of in-order
Increases scheduling scope
  Does loop unrolling transparently!
  Uses branch prediction to “unroll” branches
Examples:
  Pentium Pro/II/III (3-wide), Core 2 (4-wide), Alpha 21264 (4-wide), MIPS R10000 (4-wide), Power5 (5-wide)
Notes: Pentium Pro appeared in 1995

## Slide 6: Example: In-Order Limitations #1
In-order pipeline, three-cycle load-use penalty, 2-wide
Why not the following?
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Ld [r1] ➜ r2 | F | D | X | M1 | M2 | W |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | D | d* | d* | d* | X | M1 | M2 | W |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | D | d* | d* | d* | X | M1 | M2 | W |  |  | 
ld [r7] ➜ r4 |  | F | D | p* | p* | p* | X | M1 | M2 | W |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Ld [r1] ➜ r2 | F | D | X | M1 | M2 | W |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | D | d* | d* | d* | X | M1 | M2 | W |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | D | d* | d* | d* | X | M1 | M2 | W |  |  | 
ld [r7] ➜ r4 |  | F | D | X | M1 | M2 | W |  |  |  |  |  | 
Notes: OoO register writes, but different kind of dependence

## Slide 7: Example: In-Order Limitations #2
In-order pipeline, three-cycle load-use penalty, 2-wide
Why not the following?:
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Ld [p1] ➜ p2 | F | D | X | M1 | M2 | W |  |  |  |  |  |  | 
add p2 + p3 ➜ p4 | F | D | d* | d* | d* | X | M1 | M2 | W |  |  |  | 
xor p4 ^ p5 ➜ p6 |  | F | D | d* | d* | d* | X | M1 | M2 | W |  |  | 
ld [p7] ➜ p8 |  | F | D | p* | p* | p* | X | M1 | M2 | W |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Ld [p1] ➜ p2 | F | D | X | M1 | M2 | W |  |  |  |  |  |  | 
add p2 + p3 ➜ p4 | F | D | d* | d* | d* | X | M1 | M2 | W |  |  |  | 
xor p4 ^ p5 ➜ p6 |  | F | D | d* | d* | d* | X | M1 | M2 | W |  |  | 
ld [p7] ➜ p8 |  | F | D | X | M1 | M2 | W |  |  |  |  |  | 

## Slide 8: Out-of-Order to the Rescue
“Dynamic scheduling” done by the hardware
Still 2-wide superscalar, but now out-of-order, too
  Allows instructions to issue when dependences are ready
Longer pipeline
  In-order front end: Fetch, “Dispatch”
  Out-of-order execution core:
    “Issue”, “RegisterRead”, Execute, Memory, Writeback
  In-order retirement: “Commit”
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Ld [p1] ➜ p2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add p2 + p3 ➜ p4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor p4 ^ p5 ➜ p6 |  | F | Di |  |  |  | I | RR | X | W | C |  | 
ld [p7] ➜ p8 |  | F | Di | I | RR | X | M1 | M2 | W |  | C |  | 
Notes: didn’t save any cycles, but we are setup for more ILP

## Slide 9: Out-of-Order Pipeline
Fetch
Decode
Rename
Dispatch
Commit
Buffer of instructions
Issue
Reg-read
Execute
Writeback
In-order front end
Out-of-order execution
In-order commit

## Slide 10: Out-of-Order Execution
Also called “Dynamic scheduling”
  Done by the hardware on-the-fly during execution
Looks at a “window” of instructions waiting to execute
  Each cycle, picks the next ready instruction(s)
Two steps to enable out-of-order execution:
  Step #1: Register renaming – to avoid “false” dependencies
  Step #2: Dynamically schedule – to enforce “true” dependencies
Key to understanding out-of-order execution:
  Data dependencies

## Slide 11: Dependence types
RAW (Read After Write) = “true dependence” (true)
  mul r0 * r1 ➜ r2
  …
  add r2 + r3 ➜ r4
WAW (Write After Write) = “output dependence” (false)
  mul r0 * r1➜ r2
  …
  add r1 + r3 ➜ r2
WAR (Write After Read) = “anti-dependence” (false)
  mul r0 * r1 ➜ r2
  …
  add r3 + r4 ➜ r1
  WAW & WAR are “false”, Can be totally eliminated by “renaming”
Notes: what about RAR?

## Slide 12: Step #1: Register Renaming
To eliminate register conflicts/hazards
“Architected” vs “Physical” registers – level of indirection
  Names: r1,r2,r3
  Locations: p1,p2,p3,p4,p5,p6,p7
  Original mapping: r1p1, r2p2, r3p3, p4–p7 are “available”
  Renaming – conceptually write each register once
    Removes false dependences
    Leaves true dependences intact!
  When to reuse a physical register? After overwriting instruction is complete
MapTable |  |  |  | FreeList |  | Original insns |  | Renamed insns
r1 | r2 | r3 |  |  |  |  |  | 
p1 | p2 | p3 |  | p4,p5,p6,p7 |  | add r2,r3➜r1 |  | add p2,p3➜p4
p4 | p2 | p3 |  | p5,p6,p7 |  | sub r2,r1➜r3 |  | sub p2,p4➜p5
p4 | p2 | p5 |  | p6,p7 |  | mul r2,r3➜r3 |  | mul p2,p5➜p6
p4 | p2 | p6 |  | p7 |  | div r1,4➜r1 |  | div p4,4➜p7
Time
Notes: What can we free after this code executes? p4

## Slide 13: Out-of-order Pipeline
Fetch
Decode
Rename
Dispatch
Commit
Buffer of instructions
Issue
Reg-read
Execute
Writeback
Have unique register names
Now put into out-of-order execution structures
In-order front end
Out-of-order execution
In-order commit

## Slide 14: Step #2: Dynamic Scheduling
regfile
D$
I$
B
P
insn buffer
S
D
add p2,p3➜p4
sub p2,p4➜p5
mul p2,p5➜p6
div p4,4➜p7
Ready Table |  |  |  |  | 
P2 | P3 | P4 | P5 | P6 | P7
Yes | Yes |  |  |  | 
Yes | Yes | Yes |  |  | 
Yes | Yes | Yes | Yes |  | Yes
Yes | Yes | Yes | Yes | Yes | Yes
div p4,4➜p7
mul p2,p5➜p6
sub p2,p4➜p5
add p2,p3➜p4
and
Instructions fetch/decoded/renamed into Instruction Buffer
  Also called “instruction window” or “instruction scheduler”
Instructions (conceptually) check ready bits every cycle
  Execute oldest “ready” instruction, set output as “ready”
Time
Notes: How do we know when an insn is ready to execute? it’s inputs are ready
Why execute the *oldest* ready insn?

## Slide 15: Dynamic Scheduling/Issue Algorithm
Data structures:
  Ready table[phys_reg]  yes/no (part of “issue queue”)
Algorithm at “issue” stage (prior to read registers):
  foreach instruction:
    if table[insn.phys_input1] == ready && table[insn.phys_input2] == ready then
      insn is “ready”
  select the oldest “ready” instruction
    table[insn.phys_output] = ready
Multiple-cycle instructions? (such as loads)
  For an instruction with latency of N, set “ready” bit N-1 cycles in future

## Slide 16: Register Renaming

## Slide 17: Register Renaming Algorithm (Simplified)
Two key data structures:
  maptable[architectural_reg]  physical_reg
  Free list: allocate (new) & free registers (implemented as a queue)
    ignore freeing of registers for now
Algorithm: at “decode” stage for each instruction:
  Rewrites instruction with “physical” registers (rather than “architectural” registers
  insn.phys_input1 = maptable[insn.arch_input1]
  insn.phys_input2 = maptable[insn.arch_input2]
  new_reg = new_phys_reg()
  maptable[insn.arch_output] = new_reg
  insn.phys_output = new_reg
Notes: don’t worry about free-ing registers

## Slide 18: Renaming example
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1
r1
p1
r2
p2
r3
p3
r4
p4
r5
p5
Map table
Free-list
p6
p7
p8
p9
p10

## Slide 19: Renaming example
r1
p1
r2
p2
r3
p3
r4
p4
r5
p5
Map table
Free-list
p6
p7
p8
p9
p10
xor p1 ^ p2 ➜
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 20: Renaming example
r1
p1
r2
p2
r3
p3
r4
p4
r5
p5
Map table
Free-list
p6
p7
p8
p9
p10
xor p1 ^ p2 ➜ p6
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 21: Renaming example
r1
p1
r2
p2
r3
p6
r4
p4
r5
p5
Map table
Free-list
p7
p8
p9
p10
xor p1 ^ p2 ➜ p6
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1
Notes: why do we update the map table here?

## Slide 22: Renaming example
r1
p1
r2
p2
r3
p6
r4
p4
r5
p5
Map table
Free-list
p7
p8
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 23: Renaming example
r1
p1
r2
p2
r3
p6
r4
p4
r5
p5
Map table
Free-list
p7
p8
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 24: Renaming example
r1
p1
r2
p2
r3
p6
r4
p7
r5
p5
Map table
Free-list
p8
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 25: Renaming example
r1
p1
r2
p2
r3
p6
r4
p7
r5
p5
Map table
Free-list
p8
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 26: Renaming example
r1
p1
r2
p2
r3
p6
r4
p7
r5
p5
Map table
Free-list
p8
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 27: Renaming example
r1
p1
r2
p2
r3
p8
r4
p7
r5
p5
Map table
Free-list
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 28: Renaming example
r1
p1
r2
p2
r3
p8
r4
p7
r5
p5
Map table
Free-list
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 29: Renaming example
r1
p1
r2
p2
r3
p8
r4
p7
r5
p5
Map table
Free-list
p9
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 30: Renaming example
r1
p9
r2
p2
r3
p8
r4
p7
r5
p5
Map table
Free-list
p10
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9
xor r1 ^ r2 ➜ r3
add r3 + r4 ➜ r4
sub r5 - r2 ➜ r3
addi r3 + 1 ➜ r1

## Slide 31: Out-of-order Pipeline
Fetch
Decode
Rename
Dispatch
Commit
Buffer of instructions
(reorder buffer)
Issue
Reg-read
Execute
Writeback
Have unique register names
Now put into out-of-order execution structures

## Slide 32: Dynamic Instruction Scheduling Mechanisms

## Slide 33: Dispatch
Put renamed instructions into out-of-order structures
Re-order buffer (ROB)
  Holds instructions from Fetch through Commit
Issue Queue
  Central piece of scheduling logic
  Holds instructions from Dispatch through Issue
  Tracks ready inputs
    Physical register names + ready bit
    “AND” the bits to tell if ready
Insn
Inp1
R
Inp2
R
Dst
Ready?
Bday
Notes: Why Birthday instead of Age?

## Slide 34: Dispatch Steps
Allocate Issue Queue (IQ) slot
  Full? Stall
Read ready bits of inputs
  1-bit per physical reg
Clear ready bit of output in table
  Instruction has not produced value yet
Write data into Issue Queue (IQ) slot

## Slide 35: Dispatch Example
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9
Insn
Inp1
R
Inp2
R
Dst
Bday
Issue Queue
p1 y
p2 y
p3 y
p4 y
p5 y
p6 y
p7 y
p8 y
p9 y
Ready bits

## Slide 36: Dispatch Example
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
Issue Queue
p1 y
p2 y
p3 y
p4 y
p5 y
p6 n
p7 y
p8 y
p9 y
Ready bits
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9

## Slide 37: Dispatch Example
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
add
p6
n
p4
y
p7
1
Issue Queue
p1 y
p2 y
p3 y
p4 y
p5 y
p6 n
p7 n
p8 y
p9 y
Ready bits
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9

## Slide 38: Dispatch Example
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
add
p6
n
p4
y
p7
1
sub
p5
y
p2
y
p8
2
Issue Queue
p1 y
p2 y
p3 y
p4 y
p5 y
p6 n
p7 n
p8 n
p9 y
Ready bits
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9

## Slide 39: Dispatch Example
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
add
p6
n
p4
y
p7
1
sub
p5
y
p2
y
p8
2
addi
p8
n
---
y
p9
3
Issue Queue
p1 y
p2 y
p3 y
p4 y
p5 y
p6 n
p7 n
p8 n
p9 n
Ready bits
xor p1 ^ p2 ➜ p6
add p6 + p4 ➜ p7
sub p5 - p2 ➜ p8
addi p8 + 1 ➜ p9

## Slide 40: Out-of-order pipeline
Execution (out-of-order) stages
Select ready instructions
  Send for execution
Wakeup dependents
Issue
Reg-read
Execute
Writeback

## Slide 41: Dynamic Scheduling/Issue Algorithm
Data structures:
  Ready table[phys_reg]  yes/no (part of issue queue)
Algorithm at “schedule” stage (prior to read registers):
  foreach instruction:
    if table[insn.phys_input1] == ready && table[insn.phys_input2] == ready then
      insn is “ready”
  select the oldest “ready” instruction
    table[insn.phys_output] = ready

## Slide 42: Issue = Select + Wakeup
Select oldest of “ready” instructions
  “xor” is the oldest ready instruction below
  “xor” and “sub” are the two oldest ready instructions below
  Note: may have resource constraints: i.e. load/store/floating point
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
add
p6
n
p4
y
p7
1
sub
p5
y
p2
y
p8
2
addi
p8
n
---
y
p9
3
Ready!
Ready!

## Slide 43: Issue = Select + Wakeup
Wakeup dependent instructions
  Search for destination (Dst) in inputs & set “ready” bit
    Implemented with a special memory array circuit called a Content Addressable Memory (CAM)
  Also update ready-bit table for future instructions
  For multi-cycle operations (loads, floating point)
    Wakeup deferred a few cycles
    Include checks to avoid structural hazards
Insn
Inp1
R
Inp2
R
Dst
Bday
xor
p1
y
p2
y
p6
0
add
p6
y
p4
y
p7
1
sub
p5
y
p2
y
p8
2
addi
p8
y
---
y
p9
3
p1 y
p2 y
p3 y
p4 y
p5 y
p6 y
p7 n
p8 y
p9 n
Ready bits

## Slide 44: Note: Content Addressable Memory
A content addressable memory (CAM) is indexed by the content of each location, not by the address
  Sometimes known as associative memory
It compares an input “key” against a table of keys, and returns the location of the key in the table
  In software this might be implemented with a hash table
  Hardware hash table is also possible, but potentially slow
To search all locations in a single cycle
  You need to be able to compare the search key to all keys in the table simultaneously
    This requires a *lot* of hardware
    Fast CAMs are very hardware expensive
  If you need to be able to do multiple searches in the same cycle, the hardware requirements are even greater

## Slide 45: Issue
Select/Wakeup one cycle
Dependent instructions execute on back-to-back cycles
  Next cycle: add/addi are ready:
Issued instructions are removed from issue queue
  Free up space for subsequent instructions
Insn
Inp1
R
Inp2
R
Dst
Bday
add
p6
y
p4
y
p7
1
addi
p8
y
---
y
p9
3

## Slide 46: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 0
p7 0
p8 0
p9 0
xor RDY
add
sub RDY
addi

## Slide 47: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 0
p7 0
p8 0
p9 0
add RDY
addi RDY
xor p1^ p2 ➜ p6
sub p5 - p2 ➜ p8

## Slide 48: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 0
p7 0
p8 0
p9 0
add p6 +p4 ➜p7
addi p8 +1 ➜ p9
xor 7^ 3 ➜ p6
sub 6 - 3 ➜ p8
Notes: add depends on xor, addi depends on sub

## Slide 49: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 0
p7 0
p8 0
p9 0
add p6 + 9 ➜ p7
addi p8 +1 ➜ p9
4 ➜ p6
3 ➜ p8
Notes: use MX bypass

## Slide 50: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 4
p7 0
p8 3
p9 0
13 ➜ p7
4 ➜ p9

## Slide 51: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 4
p7 13
p8 3
p9 4

## Slide 52: OOO execution (2-wide)
p1 7
p2 3
p3 4
p4 9
p5 6
p6 4
p7 13
p8 3
p9 4
Note similarity
to in-order

## Slide 53: Renaming Revisited

## Slide 54: Re-order Buffer (ROB)
ROB entry holds all info for recovery/commit
  All instructions & in order
  Architectural register names, physical register names, insn type
  Not removed until very last thing (“commit”)
Operation
  Fetch: insert at tail (if full, stall)
  Commit: remove from head (if not yet done, stall)
Purpose: tracking for in-order commit
      Maintain appearance of in-order execution
      Needed to support:
    Misprediction recovery
    Freeing of physical registers

## Slide 55: Renaming revisited
Track (or “log”) the “overwritten register” in ROB
  Free this register at commit
  Also used to restore the map table on “recovery”
    Used for branch misprediction recovery

## Slide 56: Dynamic Scheduling Example

## Slide 57: Dynamic Scheduling Example
The following slides are a detailed but concrete example
Yet, it contains enough detail to be overwhelming
  Try not to worry about the details
Focus on the big picture:
Hardware can reorder instructions
to extract instruction-level parallelism

## Slide 58: Recall: Motivating Example
How would this execution occur cycle-by-cycle?
Execution latencies assumed in this example:
  Loads have two-cycle load-to-use penalty
    Three cycle total execution latency
  All other instructions have single-cycle execution latency
“Issue queue”: hold all waiting (un-executed) instructions
  Holds ready/not-ready status
  Faster than looking up in ready table each cycle
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [p1] ➜ p2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add p2 + p3 ➜ p4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor p4 ^ p5 ➜ p6 |  | F | Di |  |  |  | I | RR | X | W | C |  | 
ld [p7] ➜ p8 |  | F | Di | I | RR | X | M1 | M2 | W |  | C |  | 

## Slide 59: Out-of-Order Pipeline – Cycle 0
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F |  |  |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F |  |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  |  |  |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | ---
p10 | ---
p11 | ---
p12 | ---
Map Table | 
r1 | p8
r2 | p7
r3 | p6
r4 | p5
r5 | p4
r6 | p3
r7 | p2
r8 | p1
Insn | To Free | Done?
ld |  | no
add |  | no
Reorder Buffer

## Slide 60: Out-of-Order Pipeline – Cycle 1a
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di |  |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F |  |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  |  |  |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | ---
p11 | ---
p12 | ---
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p5
r5 | p4
r6 | p3
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add |  | no
Reorder Buffer
Notes: Di(spatch) includes decode and rename

## Slide 61: Out-of-Order Pipeline – Cycle 1b
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di |  |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  |  |  |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | ---
p12 | ---
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p10
r5 | p4
r6 | p3
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
Reorder Buffer

## Slide 62: Out-of-Order Pipeline – Cycle 1c
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di |  |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F |  |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | ---
p12 | ---
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p10
r5 | p4
r6 | p3
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor |  | no
ld |  | no
Reorder Buffer

## Slide 63: Out-of-Order Pipeline – Cycle 2a
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F |  |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | ---
p12 | ---
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p10
r5 | p4
r6 | p3
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor |  | no
ld |  | no
Reorder Buffer

## Slide 64: Out-of-Order Pipeline – Cycle 2b
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F |  |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
xor | p10 | no | p4 | yes | p11 | 2
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | no
p12 | ---
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p10
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld |  | no
Reorder Buffer

## Slide 65: Out-of-Order Pipeline – Cycle 2c
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I |  |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di |  |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
xor | p10 | no | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | no
p12 | no
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 66: Out-of-Order Pipeline – Cycle 3
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR |  |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I |  |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | no | p6 | yes | p10 | 1
xor | p10 | no | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | no
p10 | no
p11 | no
p12 | no
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 67: Out-of-Order Pipeline – Cycle 4
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X |  |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  |  |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR |  |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | no | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | yes
p10 | no
p11 | no
p12 | no
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 68: Out-of-Order Pipeline – Cycle 5a
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | yes
p10 | yes
p11 | no
p12 | no
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 69: Out-of-Order Pipeline – Cycle 5b
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 |  |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I |  |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  |  |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X |  |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | yes
p10 | yes
p11 | no
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 70: Out-of-Order Pipeline – Cycle 6
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 |  |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR |  |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I |  |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 |  |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | no
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 71: Out-of-Order Pipeline – Cycle 7
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W |  |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | yes
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 72: Out-of-Order Pipeline – Cycle 8a
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X |  |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR |  |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 |  |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | no
xor | p3 | no
ld | p10 | no
Reorder Buffer

## Slide 73: Out-of-Order Pipeline – Cycle 8b
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X | W |  |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR | X |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 | W |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | yes
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | yes
xor | p3 | no
ld | p10 | yes
Reorder Buffer

## Slide 74: Out-of-Order Pipeline – Cycle 9a
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR | X |  |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 | W |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | ---
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | yes
xor | p3 | no
ld | p10 | yes
Reorder Buffer
Notes: why not commit the second ld here?

## Slide 75: Out-of-Order Pipeline – Cycle 9b
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR | X | W |  |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 | W |  |  |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | yes
p4 | yes
p5 | ---
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | yes
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | yes
xor | p3 | yes
ld | p10 | yes
Reorder Buffer

## Slide 76: Out-of-Order Pipeline – Cycle 10
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR | X | W | C |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 | W |  | C |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | ---
p4 | yes
p5 | ---
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | ---
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | yes
xor | p3 | yes
ld | p10 | yes
Reorder Buffer

## Slide 77: Out-of-Order Pipeline – Done!
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
ld [r1] ➜ r2 | F | Di | I | RR | X | M1 | M2 | W | C |  |  |  | 
add r2 + r3 ➜ r4 | F | Di |  |  |  | I | RR | X | W | C |  |  | 
xor r4 ^ r5 ➜ r6 |  | F | Di |  |  |  | I | RR | X | W | C |  | 
ld [r7] ➜ r4 |  | F | Di | I | RR | X | M1 | M2 | W |  | C |  | 
Issue Queue |  |  |  |  |  | 
Insn | Src1 | R? | Src2 | R? | Dest | Bdy
ld | p8 | yes | --- | yes | p9 | 0
add | p9 | yes | p6 | yes | p10 | 1
xor | p10 | yes | p4 | yes | p11 | 2
ld | p2 | yes | --- | yes | p12 | 3
Ready Table | 
p1 | yes
p2 | yes
p3 | ---
p4 | yes
p5 | ---
p6 | yes
p7 | ---
p8 | yes
p9 | yes
p10 | ---
p11 | yes
p12 | yes
Map Table | 
r1 | p8
r2 | p9
r3 | p6
r4 | p12
r5 | p4
r6 | p11
r7 | p2
r8 | p1
Insn | To Free | Done?
ld | p7 | yes
add | p5 | yes
xor | p3 | yes
ld | p10 | yes
Reorder Buffer

## Slide 78: Handling Memory Operations

## Slide 79: Recall: Types of Dependencies
RAW (Read After Write) = “true dependence”
  mul r0 * r1 ➜ r2
  …
  add r2 + r3 ➜ r4
WAW (Write After Write) = “output dependence”
  mul r0 * r1➜ r2
  …
  add r1 + r3 ➜ r2
WAR (Write After Read) = “anti-dependence”
  mul r0 * r1 ➜ r2
  …
  add r3 + r4 ➜ r1
  WAW & WAR are “false”, Can be totally eliminated by “renaming”

## Slide 80: Also Have Dependencies via Memory
If value in “r2” and “r3” is the same…
RAW (Read After Write) – True dependency
  st r1 ➜ [r2]
  …
  ld [r3] ➜ r4
WAW (Write After Write)
  st r1 ➜ [r2]
  …
  st r4 ➜ [r3]
WAR (Write After Read)
  ld [r2] ➜ r1
  …
  st r4 ➜ [r3]
WAR/WAW are “false dependencies”
  But can’t rename memory in same way as registers
    Why? Addresses are not known at rename
  - Need to use other tricks

## Slide 81: Let’s Start with Just Stores
Stores: Write data cache, not registers
  Can we rename memory?
No (at least not easily)
  Cache writes unrecoverable
Solution: write stores into cache only when certain
  When are we certain? At “commit”
Notes: only stores => no RAW,WAR

## Slide 82: Memory Forwarding via Store Queue
Store Queue (SQ)
  Holds all in-flight stores
  CAM: searchable by address
  Age logic: determine youngest matching store older than load
Store rename/dispatch
  Allocate entry in SQ
Store execution
  Update SQ
    Address + Data
Load execution
  Search SQ identify youngest older matching store
    Match? Read SQ
    No Match? Read cache
value
address
==
==
==
==
==
==
==
==
age
Data cache
head
tail
load position
address
data in
data out
Store Queue (SQ)

## Slide 83: Store Queue (SQ)
On load execution, select the store that is:
  To same address as load
  Older than the load (before the load in program order)
Of these matching stores, select the youngest
  The store to the same address that immediately precedes the load
Notes: do example on the board

## Slide 84: Conservative Load Scheduling
Conservative load scheduling:
  All older stores have executed
    Some architectures: split store address / store data
      Only requires knowing addresses (not the store values)
  Advantage: always safe
  Disadvantage: performance (limits ILP)

## Slide 85: Load Speculation
Speculation requires three things…..
  1. When do we speculate?
  2. How do we detect a mis-speculation?
  3. How do we recover from mis-speculations?
    Squash offending load and all newer insns
    Similar to branch mis-prediction recovery
Notes: why squash all newer insns?

## Slide 86: Load Queue
Detects load ordering violations
Load execution: Write address into LQ
  Also note any store forwarded from
Store execution: Search LQ
  Younger load with same address?
    Did younger load forward from younger store? [See slide 149]
==
==
==
==
==
==
==
==
Data Cache
head
tail
load queue (LQ)
address
==
==
==
==
==
==
==
==
tail
head
age
store position
flush?
SQ

## Slide 87: Store Queue + Load Queue
Store Queue: handles forwarding, allows OoO stores
  Entry per store (allocated @ dispatch, deallocated @ commit)
  Written by stores (@ execute)
  Searched by loads (@ execute)
  Read from SQ to write data cache (@ commit)
Load Queue: detects ordering violations
  Entry per load (allocated @ dispatch, deallocated @ commit)
  Written by loads (@ execute)
  Searched by stores (@ execute)
Both together
  Allows aggressive load scheduling
  Stores don’t constrain load execution

## Slide 88: Optimistic Load Scheduling Problem
Allows loads to issue before older stores
  Increases ILP
  Good: When no conflict, increases performance
  Bad: Conflict => squash => worse performance than waiting
Can we have our cake AND eat it too?

## Slide 89: Predictive Load Scheduling
Predict which loads must wait for stores
Fool me once, shame on you-- fool me twice?
  Load instructions use aggressive strategy by default
  Keep table of load PCs that have been caused squashes
    Schedule these conservatively
  Simple predictor
  Makes “bad” loads wait for all older stores
More complex predictors used in practice
  Predict which stores loads should wait for
  “Store Sets” paper

## Slide 90: Out-of-Order: Benefits & Challenges

## Slide 91: Dynamic Scheduling Operation (Recap)
Dynamic scheduling
  Totally in the hardware (not visible to software)
  Also called “out-of-order execution” (OoO)
Fetch many instructions into instruction window
  Use branch prediction to speculate past (multiple) branches
  Flush pipeline on branch misprediction
Rename registers to avoid false dependencies
Execute instructions as soon as possible
  Register dependencies are known
  Handling memory dependencies is harder
“Commit” instructions in order
  Anything strange happens before commit, just flush the pipeline

## Slide 94
Notes: check assoc, load-use penalties

## Slide 95: OoO Execution is all around us
Example phone CPU: Qualcomm Krait 400 processor
  based on ARM Cortex A15 processor
  out-of-order 2.5GHz quad-core
  3-wide fetch/decode
  4-wide issue
  11-stage integer pipeline
  28nm process technology
  4/4KB DM L1$, 16/16KB 4-way SA L2$, 2MB 8-way SA L3$
Notes: Krait 400 released in 2012, 28nm

## Slide 96: Out of Order: Benefits
Allows speculative re-ordering
  Loads / stores
  Branch prediction to look past branches
Done by hardware
  Compiler may want different schedule for different hw configs
  Hardware has only its own configuration to deal with
Schedule can change due to cache misses
Memory-level parallelism
  Executes “around” cache misses to find independent instructions
  Finds and initiates independent misses, reducing memory latency
    Especially good at hiding L2 hits (~12 cycles in Core i7)

## Slide 97: Challenges for Out-of-Order Cores
Design complexity
  More complicated than in-order? Certainly!
  But, we have managed to overcome the design complexity
Clock frequency
  Can we build a “high ILP” machine at high clock frequency?
  Yep, with some additional pipe stages, clever design
Limits to (efficiently) scaling the window and ILP
  Large physical register file
  Fast register renaming/wakeup/select/load queue/store queue
    Active areas of micro-architectural research
  Branch & memory depend. prediction (limits effective window size)
    95% branch mis-prediction: 1 in 20 branches, or 1 in 100 insn.
  Plus all the issues of building “wide” in-order superscalar
Power efficiency
  Today, even mobile phone chips are out-of-order cores

## Slide 98: Redux: HW vs. SW Scheduling
Static scheduling
  Performed by compiler, limited in several ways
Dynamic scheduling
  Performed by the hardware, overcomes limitations
Static limitation ➜ dynamic mitigation
  Number of registers in the ISA ➜ register renaming
  Scheduling scope ➜ branch prediction & speculation
  Inexact memory aliasing information ➜ speculative memory ops
  Unknown latencies of cache misses ➜ execute when ready
Which to do? Compiler does what it can, hardware the rest
    Why? dynamic scheduling needed to sustain more than 2-way issue
    Helps with hiding memory latency (execute around misses)
  Intel Core i7 is four-wide execute w/ scheduling window of 100+
  Even mobile phones have dynamically scheduled cores (ARM A9, A15)